## Slide 1
MPMWarpYDW
GPU-Accelerated Coupled MPM-XPBD Framework for Geomaterial Failure and Fragmentation

## Slide 2
Framework Overview
Hybrid continuum-discrete simulation for progressive material failure:
  MPM Phase: Elasto-plastic deformation with damage accumulation
  Phase Transition: Automatic MPM → XPBD when damage ≥ 1.0
  XPBD Phase: Discrete particle dynamics with contact resolution
Target Applications:
  Rock avalanches and landslides
  Cave propagation and block caving
  Dynamic fragmentation under impact
  Granular flow with cohesion

## Slide 3
Material Point Method (MPM) Features
Constitutive Framework:
  Multiplicative elastoplasticity with logarithmic (Hencky) strain
  Von Mises (J₂) and Drucker-Prager plasticity models
  Return mapping in principal strain space
Damage & Phase Transition:
  Isotropic scalar damage from accumulated plastic strain
  Automatic transition to XPBD at critical damage
  Energy release: elastic strain energy → kinetic energy
Numerical Schemes:
  APIC transfer (angular momentum conservation)
  Optional RPIC for controllable damping
  Kelvin-Voigt viscoelasticity for stabilization

## Slide 4
Kinematic Framework
Deformation gradient update:
F_trial = (I + ∇v·Δt) · Fₙ
SVD decomposition:
F = U · Σ · Vᵀ
Logarithmic (Hencky) strain:
ε = log(Σ) = [log(σ₁), log(σ₂), log(σ₃)]
Volumetric-deviatoric split:
ε_vol = tr(ε)/3, ε_dev = ε − ε_vol·I

## Slide 5
Stress Computation
Kirchhoff stress:
τ = 2μ·ε + λ·tr(ε)·I
Shear modulus:
μ = E / [2(1 + ν)]
First Lamé parameter:
λ = E·ν / [(1 + ν)(1 − 2ν)]
Cauchy stress:
σ = τ / det(F)

## Slide 6
Von Mises Plasticity (J₂)
Yield criterion:
f = ‖τ_dev‖ − √(2/3)·(1−D)·σ_y ≤ 0
Associated flow rule:
Δε_plastic = Δγ · (τ_dev / ‖τ_dev‖)
Plastic multiplier:
Δγ = ‖ε_dev‖ − σ_y,eff / (2μ)

## Slide 7
Drucker-Prager Plasticity
Yield criterion:
f = ‖τ_dev‖ − √(2/3)·(1−D)·(σ_y − α·p) ≤ 0
Mean stress:
p = tr(τ)/3 (compression negative)
Non-associated flow:
Δε_plastic = Δγ · [n_dev + β·I/3]
Dilatancy parameter:
β = 0.3·α

## Slide 8
Damage Evolution & Phase Transition
Damage accumulation:
D = min(1.0, Σ(Δε_plastic) / ε_critical)
Strength degradation:
σ_y,eff = (1 − D) · σ_y
Strain energy density:
u = ½ · τ : ε
Velocity at transition:
v_release = √(2·η·u/ρ)

## Slide 9
Extended Position Based Dynamics (XPBD)
Contact Resolution:
  Spatial hash grid for O(n) neighbor search
  Iterative Gauss-Seidel constraint projection
  SOR relaxation for faster convergence
Friction Model:
  Coulomb friction with static/dynamic transition
  Velocity-based threshold for static friction
Additional Features:
  Particle cohesion (cementation)
  Particle sleeping (computational efficiency)
  Particle swelling (fragmentation bulking)

## Slide 10
XPBD Contact Mechanics
Contact constraint:
C = ‖xᵢ − xⱼ‖ − (rᵢ + rⱼ) ≥ 0
Normal correction:
Δx_n = C · n · wᵢ / (wᵢ + wⱼ)
Contact normal:
n = (xᵢ − xⱼ) / ‖xᵢ − xⱼ‖
Friction (Coulomb):
Δx_f = clamp(Δv_t·Δt, −μ·|Δx_n|, μ·|Δx_n|)

## Slide 11
MPM-XPBD Coupling Strategy
Contact-Based Momentum Transfer:
  Direct particle-particle contact forces
  Same XPBD constraint projection for MPM-XPBD contacts
  xpbd_mpm_coupling_strength scales impulse magnitude
Material Label System:
  Label 0: MPM in contact with XPBD (cannot transition)
  Label 1: MPM not in contact (can transition if D ≥ 1)
  Label 2: XPBD discrete particles
Transition Locking (prevents cascading failure):
  Reset: all label 0 → label 1 before XPBD step
  Detect: if MPM touches XPBD, set label → 0
  Transition: only label 1 can become XPBD

## Slide 12
Geostatic Initialization (K₀)
Vertical stress:
σ_v = −ρ·g·(z_top − z)
Horizontal stress:
σ_h = K₀·σ_v
Initialize F (NOT stress):
F_init = diag(exp(ε₁), exp(ε₂), exp(ε₃))

## Slide 13
Viscoelasticity (Kelvin-Voigt)
Viscous stress:
τ_visc = 2·η_shear·ε̇_dev + η_bulk·tr(ε̇)·I
Strain rate tensor:
ε̇ = ½·(∇v + ∇vᵀ)
Typical values:
η = 10³ − 10⁶ Pa·s

## Slide 14
Numerical Stability
CFL condition:
dt < α · dx / c_p (α ≈ 0.3−0.5)
P-wave speed:
c_p = √[(K + 4μ/3) / ρ]
Cell-crossing limit:
max(‖Δx‖) < 0.5 · dx

## Slide 15
Simulation Loop Structure
Big Step Loop (outer):
  Phase 1: Combined MPM+XPBD simulation
  Phase 2: XPBD-only settling (optional)
  Checkpoint save at big step boundary
Phase 1 Inner Loop:
  MPM: stress → P2G → grid ops → G2P (every dt)
  XPBD: hash grid → contacts → integrate (every dtxpbd)
  Early termination: damage stall or convergence
Phase 2 (if xpbdOnlyDuration > 0):
  XPBD steps with frozen MPM
  Sleep-based early termination

## Slide 16
Key Configuration Parameters
Time Stepping:
  dt: MPM timestep (0 = auto CFL)
  dtxpbd: XPBD timestep (10-100× dt typical)
  bigStepDuration, xpbdOnlyDuration: phase durations
Material:
  E, nu: elastic moduli
  ys, alpha: yield stress, pressure sensitivity
  strainCriteria: plastic strain for full damage
  eta_shear, eta_bulk: viscosity coefficients
Coupling:
  xpbd_mpm_coupling_strength: impulse scaling
  mpm_contact_transition_lock: prevent cascading

## Slide 17
Output Files
Particle VTP Files (ParaView time series):
  positions, radius, velocity
  damage, mean_stress, von_mises
  stress_tensor (6 components: xx, yy, zz, xy, xz, yz)
  active_label, material_label
Checkpoint Data (at big step ends):
  Full deformation gradient F, APIC matrix C
  All material properties per particle
  Enables restart: --restart path/to/checkpoint.vtp

## Slide 18
Performance Considerations
GPU Scaling:
  Particle operations: O(N) linear
  Grid operations: O(G³) with grid volume
  Contacts: O(N) with spatial hashing
Memory (approximate):
  ~500 bytes/particle, ~100 bytes/grid cell
  1M particles + 256³ grid ≈ 2.5 GB VRAM
Tuning Tips:
  Stiff materials: small dt, high xpbd_iterations
  Phase transitions: use viscosity, eff < 1.0
  Large domains: grid_particle_spacing_scale = 2.0

## Slide 19
Key References
MPM:
  Sulsky et al. (1994) - Original MPM formulation
  Stomakhin et al. (2013) - Snow simulation
Transfer Schemes:
  Jiang et al. (2015) - APIC
  Jiang et al. (2017) - SIGGRAPH MPM Course
XPBD:
  Macklin et al. (2016) - XPBD formulation
Constitutive:
  de Souza Neto et al. (2011) - Computational Plasticity
  Simo (1992) - Multiplicative plasticity

## Slide 20
Summary
GPU-accelerated MPM-XPBD coupling Multiplicative elastoplasticity with damage Automatic continuum → discrete transition Applications: geomaterial failure, fragmentation, granular flow